CONTACT TIMES FOR INSPECTIONS

(NOTICE SHALL BE GIVEN 48 HOURS IN ADVANCE)

It shall be the responsibility of the permit holder (owner or contractor) to contact the inspector’s office when the work has progressed to the point of needing an inspection.

- Excavation:  inspector to observe soil types: groundwater elevation, temporary shoring, site safety.

- Foundation:  inspector to observe location, size & shape, width, reinforcing, height of unbalanced fill, fireplace jog, ventilation, damp proofing/waterproofing, foundation drainage, and either first floor framing in place or proper bracing before backfill.

- Frame:   call after all framing is in place the sub trades have finished all cutting, drilling and notching.  Inspector to observe species & grad, spans, connections, cutting & notching; and fire stopping (AFTER INSPECTION AND SIGN OFF FROM SUB-TRADE INSPECTORS)

- Sub-trade Inspections:  call appropriate inspector for individual inspections including, but not limited to: Plumbing, Gas, Electrical, Oil Burner, Fire Department, Health Department.

- Fireplace/chimney:  call following completion of firebox, throat and first flue set (mandatory inspection point)

- Insulation:  after insulation is in place; inspector to observe insulation type, vapor barrier, and R-values.

- Mechanical:  inspection of duct installation (for type and fastening), furnace plenum, hydronic piping, wood & pellet stoves, dryer vents, bath exhaust fans, heat pumps, etc.

- Finish:  call after sub-trade inspectors have signed for final approvals and building or parts there of, are ready for occupancy and/or use

Contact Telephone Numbers:

| Inspection Service | Inspectors Name | Contact Telephone Number |
| --- | --- | --- |
| Building Inspection | Brianna Skowyra | 978-249-3834 |
| Electrical Inspection | Gary Terroy | 978-249-2868 |
| Gas Inspection | Daniel Joly | 978-249-9583 |
| Plumbing Inspection | Daniel Joly | 978-249-9583 |
| Oil Burner Inspection | John Duguay | 978-249-8275 |
| Fire Department Inspection | John Duguay | 978-249-8275 |
| Board of Health | Deborah Karan | 978-249-7934 |
| Conservation Commission | Bob Muzzy | 978-249-3734 |
| Dig Safe | www.digsafe.com | 888-344-7233 (72 hr notice) |